## Slide 1
Integrated Sensing & Database Architecture for White Space Networking
Sumit Roy
Dept. of Electrical Eng.
U. Washington, Seattle
roy@ee.washington.edu
www.ee.washington.edu/research/funlab

## Slide 2: uw SPECTRUm OBSERVATORY INSIGHTS FROM BUILDING AN OPEN SOURCE Spectrum DATABASE FOR TV WHITE SPACE
http://specobs.ee.washington.edu

## Slide 3
Main Take-aways
Databases are based on (predictive) propagation models
- these are imperfect at best, and at worst – significantly
inaccurate (urban canyons and indoors, in particular)
  For TVWS, the FCC mandated the use of F-curves for primary
  protection, already we can do better (use Longley-Rice) !
Current Databases leave a lot to be desired in terms of
lack of useful supporting analytics; secondary interference
modeling is missing (FCC rules only focused on primary
protection!)
Hence purely using Databases (as per present FCC) to
estimate availability of White Spaces is inadvisable
 need to involve local spectrum measurements to
complement Databases!

## Slide 4: UW Spectrum Observatory Database - Concept Overview
http://specobs.ee.washington.edu/

## Slide 5: UW SpecObs Architecture

## Slide 6: SpecObs Web GUI (Google Maps API)

## Slide 7
Query data by various options
Show TV White Space Data
(Example Data for
latitude : 40.3832, longitude : -96.0511)
Coverage region of each TV tower for channel 10

## Slide 8: TV White Space Analytics (US)
# of available TVWS channels in the U.S. acc. to location

## Slide 9: SpecObs Database Functions
Calculates noise floor and capacity based on Longley-Rice P2P mode, for each predicted WS channel
Shows details of each occupied channel

## Slide 10: FCC - OET Bulletin 69
  Developed in 1990s for the transition from
  analog to digital
  Determining coverage area
  and interference using two propagation models
  - FCC F-Curves and Longley-Rice model
  Coverage area
    Calculates TV service contours by using F-Curves
  Evaluation of TV service
    Predicts field strength at the receiver location with Longley-Rice model
    Analyzes interference based on predicted field strength
  “Longley-Rice Methodology for Evaluating TV Coverage and Interference”

## Slide 11: FCC Method: F-Curve
  F-Curve Functions
    Provide two functions for different outputs - field strength and distance
Input Parameters
Distance (TX and RX)
Channel
Propagation Curve
ERP
TX HAAT
Output Parameters
Field Strength (dBuV/m)
CalcFieldStrength()
Input Parameters
Desired Field Strength
Channel
Propagation Curve
ERP
TX HAAT
Output Parameters
Distance (km)
CalcDistance()

## Slide 12: What are F-Curves?
Frequency bands
  Low VHF (channel 2-6)
  High VHF (channel 7-13)
  UHF (channel 14-51)
Time and Location
  F(50, 50)
    50% of Location and 50 % of Time
    Used for Analog TV
  F(50, 90)
    50% of Location and 90 % of Time
    Used for Digital TV

## Slide 13: FCC Defined Coverage Area
TV Type | Channel 2- 6 | Channel 7 – 13 | Channel 14 - 51
Analog | 47 | 56 | 64
Digital | 28 | 36 | 41
  TV station’s noise-limited contour
 Defined with F-Curve and Field Strength Threshold
Table 1. Field Strength (dBuV/m) Threshold to define TV coverage
Coverage Area computed by F-Curve (KIRO-TV in Seattle)

## Slide 14: FCC Method: Coverage Area (F-Curve)
= CalcDistance(, , , Channel, Curve) for i = [0:359]
i = azimuth (0 – 359)
= Distance between TX and RX
= Desired field strength (threshold)
= Power for ,
TV Station
= Coordinate of distance and azimuth i from TV station
= TV station’s coordinate
TV Station
Draw contour by connecting and complete coverage
Di
θi
TV Station

## Slide 15: FCC Method: Issues with F-Curve
Incomplete use of terrain data
  Calculate average terrain elevations (every 100 m) between 3.2 and 16.1 km from the transmitter
  Transmitter HAAT = Antenna Height (AMSL) – Avg. Elevation
  Problem: Only considers nearby elevation (up to 16.1km)
    How about a terrain obstacle at distance > 16.1 km?
    Does not take account into diffraction due to LoS obstruction
TV Transmitter
TV Receiver
3.2 km
16.1 km

## Slide 16: Longley-Rice model for Path LOSS PREDICTION IRREGULAR TERRAIN MODEL
Statistical/semi-empirical model
- includes terrain specific inputs
- Empirically weights loss components from knife
edge diffraction with those from multipath propagation
Adopted as a standard by the NTIA
  Wide range of applicability: 20 MHz- 40 GHz;
upto 2000 Km
low & high altitude scenarios
Many software implementations available commercially
Includes most relevant propagation modes
  multiple knife & rounded edge diffraction (irregular terrain),
  atmospheric attenuation, tropospheric propagation

## Slide 17: Longley-Rice Model
L-R P2P mode
  Input – Elevation values every 100 m between TX and RX used
  Output – Field Strength (dBuV/m)
  Accounts for LOS, diffraction, multipath effects from irregular terrain
  The figures show impact of terrain elevation
Elevation of azimuth 0 degree (KIRO-TV)
Field strength of azimuth 0 degree (KIRO-TV)

## Slide 18: Iconectiv(Telcordia) prism.telcordia.com/tvws/main/index.shtml
The location (40.68691, -74.39718), Portable TVBDs (40 mW)
WS Channel Result [22,27,32,42,46,47,48,49]

## Slide 19: Experimental Results (Bell Labs, NJ)
Sensed TV Spectrum during 15 hours (7:00 PM – 10:00 AM)
Scan every minute for 30 seconds
Location {Lat : 40.68691, Long : -74.39718} inside a lab
Portable Device Channel [21-51] except 37
Rank | Channel | Avg RSSI (dBm) | Rank | Channel | Avg RSSI (dBm) | Rank | Channel | Avg RSSI (dBm)
1 | 22 | -118.9723 | 11 | 33 | -111.2699 | 21 | 39 | -108.1211
2 | 21 | -118.6064 | 12 | 36 | -111.2457 | 22 | 48 | -107.5307
3 | 23 | -115.1224 | 13 | 25 | -111.0240 | 23 | 30 | -107.3896
4 | 38 | -113.6022 | 14 | 27 | -110.4862 | 24 | 45 | -106.9321
5 | 26 | -112.3652 | 15 | 41 | -110.4683 | 25 | 47 | -106.8143
6 | 24 | -112.1441 | 16 | 32 | -110.4371 | 26 | 44 | -106.5032
7 | 34 | -112.0327 | 17 | 43 | -110.3331 | 27 | 46 | -106.2404
8 | 31 | -111.8473 | 18 | 40 | -110.2666 | 28 | 28 | -106.1710
9 | 49 | -111.5402 | 19 | 50 | -109.8531 | 29 | 29 | -99.6048
10 | 42 | -111.4835 | 20 | 35 | -109.2027 | 30 | 51 | -94.4028
Ranking with Average RSSI for the experiment time, Red : WS Channels from official DBAs

## Slide 20: Coverage Area with Longley-Rice
  Method
    Calculate the maximum distance to threshold (i.e. field consistently < threshold thereafter) for each azimuth
    Connect max. points over azimuth to obtain coverage perimeter
  Note on result
    Typically very irregular coverage perimeter but also provides over-optimistic service area.
Example of L-R Coverage
(Digital Full Power TV,
Call Sign: KIRO-TV, Channel: 39)

## Slide 21: Coverage Area: L-R P2P + Classification
Incorporate classification algorithm
  Calculate field strength at dense points around transmitters with L-R P2P mode
  Use K-NN algorithm to classify points as WS or within service area
Estimation of L-R field strength
(KIRO-TV)
Comparison of coverage (KIRO-TV)
L-R P2P Vs F-Curve

## Slide 22: K-NN Classification and Validation
KNN Classification
  Labels estimation samples (L-R estimated points)
N-fold Cross Validation
  Divides samples randomly into N subsets Yi = {1,2,…,N} and # of samples in each subset = M
  Each set becomes a testing set, and samples in a testing set Yi = {x1,x2,…,xm} and their labels
  All other N-1 subsets become training samples
  Finds K nearest neighbors for testing samples, and returns the majority vote of their labels
  Calculates error rates and run N times validation
  and
Find optimal K to minimize error rate with cross validation

## Slide 23: KNN Classification
Definition of Error Types
  Type I Error: classification result is occupied when it is actually white space
    }
  Type II Error: classification result is white space when it is actually occupied
    }
Target Function to find the optimal K
  KIRO-TV, Seattle
  Run 10-fold cross validation for KNN
  K = [1:50]
  Optimal K = 8
    Total error rate = 12.435 %
    Type I (4.037 %) + Type II (8.398 %)

## Slide 24: K-NN Classification: choice of K?
  Large K: Draw one coverage, but higher prob. of miss classification
  Optimal K (relatively small): Create many holes, but optimum for miss classification
L-R coverage (K = 8)
Optimal K Total error rate = 12.435 %
Type 1 (4.037 %) + Type 2 (8.398 %)
L-R coverage (K = 113)
The smallest K to get one coverage
Total error rate = 15.086 %
Type 1 (4.573 %) + Type 2 (10.513 %)

## Slide 25: Coverage Area Prediction: SINR based
Calculate
for each Cell
> Threshold ?
Calculate SINR()
Service Cell
- Desired station (D)
- Undesired station (U)
Calculate
for each Cell
Yes
No-service
Cell
No
Run KNN classification
N = kTB = -106 dBm/6MHz
Determine Boundary
  Consider interference from other TV transmitters
  Determine service reception based on SINR threshold
  Use Longley-Rice P2P mode to calculate signal strength

## Slide 26: Example
Evaluation of the coverage computed with F-Curve
  Two nearby DTV stations operating in co-channel (channel 39)
  Their TV coverages are partially overlapped
  High possibility of co-channel interference
Desired Station
Channel: 39 Call sign: WMYT-TV Service type: DT ERP: 225.0 kW HAAT: 571.0 m Antenna Type: ND Coordinate: 35.36222,-81.15528
Undesired Station
Channel: 39 Call sign: WKTC Service type: DT ERP: 500.0 kW HAAT: 391.0 m Antenna Type: DA Coordinate: 34.11611,-80.76417
Coverage area for WMYT-TV and WKTC (F-Curve)

## Slide 27: Results (Our Approach)
Result of TV Coverage (WMYT-TV)
  Calculates SNR-based coverage and SINR-based coverage
  Run KNN algorithm to compute a closed-loop coverage
  SINR-based coverage loses some service regions of WMYT-TV due to interference from WKTC
WMYT-TV service region and coverage based on SNR threshold (16 dB) and K = 250
Total error rate = 15.376 %
Type 1 (8.218 %) + Type 2 (7.158 %)
WMYT-TV service region and coverage based on SINR threshold (15.16 dB) and K = 250
Total error rate = 13.916 %
Type 1 (6.491 %) + Type 2 (7.425 %)

## Slide 28: Results (Our Approach)
Comparison of TV Coverage
  SINR-based coverage of two stations are distinct
  Our approach shows better estimation of coverage
SNR-based Coverage comparison
for WMYT-TV and WKTC
SINR-based Coverage comparison
for WMYT-TV and WKTC

## Slide 29
Towards Data-driven White Space Maps
State of Spectrum Measurements very spotty
- data not publicly available
- no continuous monitoring
- point data, almost no driving data (i.e. area coverage)
 need robust vehicle-friendly platforms and commitment to
sustained open source data campaigns !

## Slide 30: System Architecture
Sensor Nodes
IP Network
Spectrum
Database
Management
Server
Secondary TVWS Networks (with sensing capability)
Access Point
Client
- Report sensing data
- Request channel
- Compute and store sensing data
- Provide available WS channels
(Longley-Rice propagation model + spectrum sensing)
Dynamic Spectrum Database
Secondary TVWS Networks (without sensing capability)
Response WS list
(spectrum sensing)
Response WS list
(L-R model)

## Slide 31: Mobile-sensor based Data Collection
Spectrum Sensor
Access Point
Wi-Fi Interface Card
Wi-Fi to WhiteSpace
Translator
Daemon Module
(Python)
PyRF Library
ThinkRF WSA4000
Database
Server
Dell PowerEdge 2950
UHF Antenna
GPS

## Slide 32: Spectrum Sensing
Daemon Module
  Run spectrum sensing and collect I/Q Samples in UHF bands
  Perform windowing (Hanning, Hamming, Blackman, Bartlett-Hann)
  FFT -> convert signal into frequency domain
  Report the result to the database server periodically
Spectrum Sensor
Window Function
Calibration
I/Q Sample
<FREQ (Hz), RSSI (dBm)>
Sensing UHF TV bands
(470-698 MHz)
Database
Server
Daemon Module
Tagged by time and location
Upload as CSV files
FFT
(average N times scan)

## Slide 33: Mobile Data Collection (near Bell Labs, NJ)
Measured RSSI for TV spectrum tagged by location and time
Expect RSSI with new location

## Slide 34: TVWS Detection Algorithm
IF channel C in the FCC ruling (PLMRS channel, wireless mic. channel) THEN
LLM = C or LWMC = C
ELSE
He = 0; Hp = 0
IF Energy T > threshold THEN
He = 1
IF Pilot P > threshold Pth THEN
Hp = 1
END
END
END
IF He = 1 AND Hp = 1
Hd = 1
LDTV = C or LATV = C
ELSE
Hd = 0
LWS = C
END
END
DTV
Analog TV

## Slide 35: Energy Detector
- Two hypotheses
n = 1, 2, …, N
- Test Statistics
- Distribution of T (CLT)
- Probability of False Alarm and Detection
Use Gaussian Distribution
- Decision Threshold
- Constant False Alarm Rate (CFAR)
In order to decide threshold , choose we want to achieve.
- Parameters for implementation
Average noise level
= -159 dBm/Hz = -91.21 dBm over 6MHz
(Spectrum Sensor : ThinkRF WSA4000)
= -91.21 dBm, = 0.1, = 10,
Decision Threshold = -79.03 dBm

## Slide 36: Pilot Detector
FFT-based Pilot Detector
- Formula
=
- Test Statistics
FINAL  AND Rule to decide primary presence
= AND
= 0 (white space channel)
= 1 (occupied channel)
DTV Pilot Signal

## Slide 37: Primary Detection Algorithm
Energy & Pilot Detection
FCC rules
Mark as white space channel
Pg = 0?
Pg = Logical AND
Last Channel?
Terminate
Loop [Channel List]
Delete from white space channel

## Slide 38: Experiment Result
Total observation time: 15 hours (7:00 PM – 10:00 AM)
  Sensing Duration = 30 seconds per every minute
  About 800 observation samples
Sensing Location: the Bell Labs (fifth floor) in NJ
  Latitude : 40.68691, Longitude : -74.39718
Run spectrum sensing for portable device: Channel [21-51]
AND Rule threshold = 90% (occupancy of channel during observation time)
WS channels from SpecObs: 25 channels
  Including all DBA WS channels
  [22,23,24,25,26,27,28,30,31,32,33,34,36,38,40,41,42,43,44,45,46,47,48,49,50]
WS channels from DBA: 8 channels
  [22,27,32,42,46,47,48,49]

## Slide 39: Experiment Results
Channel | Avg RSSI (dBm) | Energy Detection (%) | Pilot Detection (%) | Category | Channel | Avg RSSI (dBm) | Energy Detection (%) | Pilot Detection (%) | Category
51 | -65.43 | 100 | 100 | DTV | 27 | -81.49 | 0.0 | 0.0 | WS
29 | -70.64 | 100 | 99.88 | DTV | 32 | -81.55 | 15.84 | 0.0 | WS
28 | -77.20 | 99.65 | 2.72 | WS | 25 | -82.15 | 0.72 | 0.0 | WS
46 | -77.22 | 100 | 0.0 | WS | 36 | -82.24 | 0.48 | 0.0 | WS
44 | -77.55 | 100 | 0.0 | WS | 33 | -82.31 | 0.35 | 0.24 | WS
47 | -77.74 | 100 | 0.0 | WS | 49 | -82.47 | 0.0 | 0.0 | WS
45 | -77.96 | 100 | 0.0 | WS | 42 | -82.53 | 0.0 | 0.0 | WS
30 | -78.39 | 79.08 | 41.25 | WS | 34 | -82.84 | 0.48 | 4.09 | WS
48 | -78.50 | 85.34 | 14.89 | WS | 31 | -83.07 | 0.0 | 0.0 | WS
39 | -79.10 | 17.26 | 0.0 | WMC | 24 | -83.25 | 0.0 | 7.33 | WS
35 | -80.25 | 4.49 | 0.0 | WMC | 26 | -83.45 | 0.35 | 0.0 | WS
50 | -80.89 | 0.0 | 0.0 | WS | 38 | -84.62 | 0.00 | 0.0 | WS
40 | -81.23 | 1.06 | 0.0 | WS | 23 | -86.15 | 0.0 | 3.9 | WS
43 | -81.41 | 0.12 | 0.0 | WS | 21 | -89.63 | 0.0 | 0.0 | LM
41 | -81.47 | 0.0 | 0.0 | WS | 22 | -90.05 | 0.0 | 0.0 | WS
LM: Private Land Mobile Radio Service Channel WS: White Space Channel, WMC: Wireless Microphone Channel, DTV: DTV Channel
Predictions (DB) are often conservative and
may NOT protect primaries &
may lead to missed spectrum usage opportunities

## Slide 40
Role of Spatial Stochastic Modeling for Signal Mapping
Current approaches do not account for spatial
correlations in the received signal
Uniform spatial sampling is impossible !
Hence, given RSSI samples over some set:
 use measurement data to estimate the
spatial statistics (variogram) and model fit
followed by spatial interpolation (Kriging) to points
where no measurement is available.
Then conduct classification as before.

## Slide 41: General Approach
Pre-processing
Empirical variogram estimation
Empirical variogram modeling
Model selection via cross-validation
Interpolation
(Ordinary Kriging)
Radio Environment Map/Protection Region
(Semi) variogram estimation
Sampling

## Slide 42: Empirical Semivariogram Estimation
Classical estimator:
  where 𝑁(𝒉) is the total number of sample pairs whose separation is approximately equal to 𝒉.
  How to construct ?
  Specify distance bins with equal lengths;
  For each bin, find all pairs whose pair-wise separation falls into the bin;
  Take the average of squared differences of pairs for each bin;
  Source: NOTEBOOK FOR SPATIAL DATA ANALYSIS by Tony E. Smith

## Slide 43: Empirical Semivariogram Modeling
Fit with parametric models
  Models available: exponential, spherical, Gaussian, cubic etc.
Least Square Fitting
  Ordinary LS (OLS) – equal weights
  Weighted LS (WLS) – weights ~ N(h)

## Slide 44: Seattle Drive Data (Jun 2014)
Location/Area: North Seattle
  Three days: June 6/11/12
  240+ locations
  4.6 km x 5 km
Setup
  USRP B210 (GNURadio) + a laptop
  Digital TV antenna (gain = 3 dBi) installed on top of a van
  I/Q samples of CH 21 – 51 are collected
  Energy detection is realized through post-processing
  Reported noise level = -82.16 dBm

## Slide 45: Propagation models v.s. Kriging
Example: CH 38
Two models: Longley-Rice ITM and F-Curve
Ordinary Kriging is applied
Distance:
9 km

## Slide 46: Evaluation
CH NO. | Metric | CH 25 | CH 38 | CH 50
Tower Dist. To Region | N/A | 10.6 km | 9 km | 35 km
L-R | Mean Error | 31.59 | 27.86 | 14.99
 | S. D. | 7.42 | 7.45 | 12.93
F-Curve | Mean Error | 27.27 | 24.93 | 8.95
 | S. D. | 6.80 | 8.97 | 9.10
Kriging | Mean Error | -0.02 | 0.01 | 0.01
 | S. D. | 5.48 | 6.26 | 5.96
Observations:
  L-R and F-Curve overestimates RSS up to 30 dB.
  Kriging is based on local sensing data, and hence more accurate than L-R and F-Curve models.

## Slide 47: Kriging vs KNN – Boundary Estimation
Setup
  CH 35 exhibits weak signal strengths in Northern Seattle.
  Measurement results are assumed to be the ground truth.
  A Location x is a white space (labeled as 1) if , otherwise, a non-white space (labeled as 0).
~120 km
  Example of training/testing sets. Data are randomly divided into training/testing sets equally. Red dots denote training samples, and blue dots testing samples.

## Slide 48: Metrics
Type I Error: a channel is predicted to be occupied, when the primary is absent (ground truth).
Type II Error: a channel is predicted to be available, when the primary is present (ground truth).
Note that per FCC ruling, secondary devices should avoid any interference with primary users. Hence, the type II error rate is more important.

## Slide 49: Evaluation
Thr. (dBm) | -82 | -81.9 | -81.8 | -81.7 | -81.6 | -81.5
Kriging () | 0.65 | 0.47 | 0.39 | 0.24 | 0.22 | 0.18
 | 0.07 | 0.09 | 0.24 | 0.09 | 0.23 | 0.13
KNN () | 0.19 | 0.25 | 0.20 | 0.14 | 0.19 | 0.06
 | 0.25 | 0.18 | 0.42 | 0.45 | 0.32 | 0.44
Thr. (dBm) | -82 | -81.9 | -81.8 | -81.7 | -81.6 | -81.5
 | 0.65 | 0.47 | 0.39 | 0.24 | 0.22 | 0.18
 | 0.07 | 0.09 | 0.24 | 0.09 | 0.23 | 0.13
 | 0.19 | 0.25 | 0.20 | 0.14 | 0.19 | 0.06
 | 0.25 | 0.18 | 0.42 | 0.45 | 0.32 | 0.44
  Kriging and KNN boundaries when threshold = -81.8 dBm.
  Red/blue shadows are predicted coverage/ non-coverage regions.
  Red dots are testing samples that are not white spaces, and blues are testing white spaces.

## Slide 50
Conclusions
Work in Progress  just the beginning in Large Scale Radio Mapping!