## Slide 1: GHz-Wide Realtime Spectrum Sensing Using MHz-Wide Radios
Lixin Shi (MIT)
Victor Bahl (Microsoft), Dina Katabi (MIT)

## Slide 2: Today’s Spectrum Occupancy Report
Microsoft Spectrum Observatory (08/03/2013 – 08/08/2013)

## Slide 3: Today’s Spectrum Occupancy Report
Microsoft Spectrum Observatory (08/03/2013 – 08/08/2013)
1755MHz – 1800MHz
(Air Force)

## Slide 4: Today’s Spectrum Occupancy Report
Microsoft Spectrum Observatory (08/03/2013 – 08/08/2013)
3.5GHz-3.6GHz
(Radar Band)
Today’s spectrum occupancy reports miss important signals
Why?

## Slide 5
Today:
Sequential sensing with MHz BW
Ideally:
Realtime sensing with GHz BW
Freq
Time
Cheap, practical
Miss important signals
Freq
Time
Capture all signals
Costly, and effectively impractical
Can we use MHz radios but capture all signals?

## Slide 6: Intuition: Scan Bands to Maximize the Probability of Detecting Signals
Example 1:
Always-on
(TV signal)
Example 2:
Periodic
(Radar Signal)
Example 3:
Dynamic
(Amateur Radio)
638 MHz
632 MHz
3500
MHz
3600
MHz
436.0
MHz
435.5
MHz
Time (s)
Brief Check
Brief Check
Random Check
Use all of the saved time

## Slide 7: SpecInsight
Uses tens-of-MHz radios to scan a multi-GHz spectrum
Evaluated in 6 US cities
Captures signals even if their occupancy is very small

## Slide 8: SpecInsight Architecture
Learning Spectrum Patterns
Scheduling Based on the Patterns
Pattern is a representative time-frequency chunk

## Slide 9: SpecInsight Architecture
Learning Spectrum Patterns
Scheduling Based on the Patterns
Pattern is a representative time-frequency chunk

## Slide 10: Learning Patterns
FCC Band
Pattern 1
Pattern 2
CDF
Extract the patterns
Detect the distribution of occurrence

## Slide 11: Learning Patterns
FCC Band
CDF
Detect the distribution of occurrence
Pattern 1
Pattern 2
Extract the patterns

## Slide 12: Extracting Patterns
f
t
f
t
Input samples
Patterns
f
t
Dividing
Cluster!

## Slide 13: Identifying Patterns
f
t
f
t
Input samples
Patterns
f
t
Dividing
Cluster 1
Cluster 2
Noise
Clustering

## Slide 14: Learning Patterns
FCC Band
CDF
Detect the distribution of occurrence
Pattern 1
Pattern 2
Extract the patterns

## Slide 15: Learning Patterns
FCC Band
Pattern 1
Pattern 2
Extract the patterns
CDF
Detect the distribution of occurrence

## Slide 16: Pattern Occurrence Distribution
…
CDF()
Distribution
Parameters:
 Period
 Dynamism

## Slide 17: SpecInsight Architecture
Learning Spectrum Patterns
Scheduling Based on the Patterns
Pattern is a representative time-frequency chunk

## Slide 18: Scheduling Sensing Based on Patterns
CDF()
Sensing Schedule
Expected
occurrence
When to sense the next?
Proportional to

## Slide 19: Exploitation vs. Exploration
Learning Spectrum Patterns
Scheduling Based on the Patterns
Exploration
Exploitation
What is the optimal balance?

## Slide 20: Solution: Multi-Armed Bandit
…
K bandit machines
Each machine will give some random rewards
The rewards follow some distribution
The distribution is not known a priori
Each time only one machine can be chosen
[1] J. Vermorel and M. Mohri. Multi-Armed Bandit Algorithms and Empirical Evaluation, In ECML, 2005.

## Slide 21: Solution: Multi-Armed Bandit
…
K bandit machines
Each machine will give some random rewards
The rewards follow some distribution
The distribution is not known a priori
Each time only one machine can be chosen
How to maximize the rewards?
K frequency bands
Each band might have signals at any time
The signals follow some pattern
The pattern is not known a priori
Each time only one band can be sensed
How to maximize the signals captured?
SpecInsight optimizes the scheduling using the multi-armed band algorithm.
[1] J. Vermorel and M. Mohri. Multi-Armed Bandit Algorithms and Empirical Evaluation, In ECML, 2005.

## Slide 22: SpecInsight’s Implementation
USRP1(SBX)
400-4400MHz
USRP2(WBX)
50-2200MHz
Outdoor Antenna
Per USRP:
- Sampling Rate: 50 MS/s
- Instant BW: 40MHz
Indoor USRPs
Outdoor Antenna

## Slide 23: Evaluated in Six Locations
Boston, MA
Amherst, MA
Upper Arlington, OH
Redmond, WA
San Francisco, CA
New York City, NY
One week of data

## Slide 24: Accuracy
Comparing SpecInsight with today’s sequential scanning from 50MHz to 4.4GHz for exactly the same time / bandwidth resources
On average, our error is 10x smaller than today’s sequential scanning.

## Slide 25: Understanding why SpecInsight is more accurate
SpecInsight saved more than 95% of the time to be spent on the dynamic classes

## Slide 26: Spectrum Analytics Chart

## Slide 27: Spectrum Analytics Chart
Frequency Hopping, Always On
Fixed Frequency, Always On
Frequency Hopping, Dynamic
Fixed Frequency, Fixed Cycle
Wide-Band, Fixed Cycle
Fixed Frequency, Dynamic
Wide-Band, Dynamic
Freq Hopping, Dynamic
Wide-Band, Fixed Cycle
Fixed Freq, Fixed Cycle

## Slide 28: Spectrum Analytics Chart
Frequency Hopping, Always On
Fixed Frequency, Always On
Frequency Hopping, Dynamic
Fixed Frequency, Fixed Cycle
Wide-Band, Fixed Cycle
Fixed Frequency, Dynamic
Wide-Band, Dynamic
38% of spectrum looks completely empty while they are used

## Slide 29: Occurrence Distributions
Chart: 
| Always-On | Fast-Periodic | Slow-Periodic | Dynamic
Sales | 0.3024 | 0.1821 | 0.1649 | 0.3505

## Slide 30: Occurrence Distributions
65% of the bands have technologies that are either always-on or transmit periodically
Chart: 
| Always-On | Fast-Periodic | Slow-Periodic | Dynamic
Sales | 0.3024 | 0.1821 | 0.1649 | 0.3505
65%

## Slide 31: Occurrence Distributions
Chart: 
| Always-On | Fast-Periodic | Slow-Periodic | Not Highly Dynamic | Highly Dynamic
Sales | 0.3024 | 0.1821 | 0.1649 | 0.3005 | 0.05
65% of the bands have technologies that are either always-on or transmit periodically
Among the dynamic patterns, only 5% are highly dynamic
5%

## Slide 32: Conclusion
SpecInsight resolves the conflict of obtaining full spectrum details while using limited-bandwidth, cheap radios.
SpecInsight reveals new information about spectrum patterns providing deeper understanding of both occupancy and spectrum usage.