## Slide 1: TxMiner: Identifying Transmitters in Real World Spectrum Measurements
Mariya Zheleva
University at Albany, SUNY

## Slide 2: Spectrum Allocation
100%

## Slide 3: Spectrum Assignment (in Washington State)
According to FCC dashboard:
  A total of 2498MHz (77.3%) appear unassigned.
  Assignments are granted to 88 unique entities in Washington.
  50% of all licenses are owned by 10 companies.
14.7% New Cingular Wireless PCS
8.9% AT&T Mobility
6.8% T-Mobile License
6.6% Cellco Partnership
5.8% Verizon Wireless
4.2% Clearwire Spectrum Holdings
2.9% American Telecasting Development
2.1% Seattle SMSA Limited Partnership
2.1% Cricket License Company
1.8% NSAC
UHF TV
Cellular 698-902MHz
Cellular 628-960MHz
PCS Cellular
1700-2200MHz
Broadband
and
Educational
Radio Services
(BRS and EBS)
Source: http://www.fcc.gov/developers/spectrum-dashboard-api

## Slide 4: Occupancy
How much spectrum is occupied?
How good is the available spectrum for DSA?
  What transmitters are occupying the spectrum?
??%

## Slide 5: Why Do We Care About Occupancy?
Help regulators, e.g. FCC, to open up additional spectrum:
  Who is using the spectrum?
  How much bandwidth can the system get using DSA?
Help interested parties make a case for release of DSA spectrum.
Inform DSA techniques in different spectrum bands:
  Which bands are continuously available and which are periodically available?
    What implications would the type of availability have on DSA devices.
  Will spectrum sensing work?
  How accurate is a geo-location database?
  How much interference will it cause on the primary user?
Policy
Technology

## Slide 6: TxMiner Goal
Power Spectral Density Graph
PSD, dBm/Hz
Frequency, MHz
Transmissions:
  Center frequency
  Number of transmitters
  Bandwidth
  TDMA/FDMA
  Mobility
  Direction

## Slide 7: TxMiner Applications
TX periodicity
TX bandwidth
Mobile TX over time
Primary or Secondary
TxMiner-enhanced
DSA Database
Secondary User
Network
1) Spectrum availability?
2) Spectrum availability +
Transmitter Characteristics
3) Bandwidth X
satisfies user
demand
Geo-location
database

## Slide 8: Key Insight
Measured signal distributions tell us about channel occupancy.
Stationary sensor. Wide-range TV broadcast service.
Stationary sensor.
Short-range
frequency-hopping
transmission.
Mobile sensor.
Wide-range TV
broadcast service.

## Slide 9: Key Insight
Measured signal distributions tell us about channel occupancy.
Idle TV channel
  Mean -108dBm
Occupied TV channel
  Mean -70dBm
Two occupied TV channels
  Bimodal distribution
Bluetooth
  Long tail at high PSD
Mobile transmitter
  Large variation
  Stationary: Δ=10dBm
  Mobile: Δ=25dBm

## Slide 10: Key Insight
Why a Distribution?

## Slide 11: Gaussian Mixture Models
Unsupervised machine learning.
Captures sub-populations in a
given population.
Fit goodness based on
minimization of BIC (Bayesian
Information Criterion).
Each Gaussian is characterized with a weight ωg, a mean µg and a variance σg:
  ωg – how represented is a Gaussian in the measured data
  µg – the mean of the measured signal
  σg – the variance of the measured signal
Measured PSD over
frequency and time.
A histogram of measured
signal with fitted Gaussians
as per GMM.

## Slide 12: Mining Transmitters
Ready to extract some transmitters?
Post-processing is necessary to:
  Determine components due to the same transmission.
  Extract transmitter characteristics.
More than one Gaussian per transmitter.

## Slide 13: Mining Transmitters: Algorithm
Noise floor
Anticipated transmissions
GMM
From raw PSD to GMM
Association probabilities
Transmitter signature extraction
Smooth association probabilities
Extract signatures
Mine transmitters

## Slide 14: Transmitter Signature Extraction
Time
Frequency
Frequency
Same signature => same transmitter
3D space (time, frequency, PSD)
2D space (frequency, Signature)

## Slide 15: Evaluation
TxMiner implemented in MATLAB.
Evaluation goals:
  Accuracy in occupancy detection.
  Transmitter count and bandwidth.
  Comparison with edge detection.

## Slide 16: Measurement Setup
RfEye spectrum scanner
manufactured by CRFS*.
* http://www.crfs.com/products/rf-sensor-rfeye-node/
Multi-polarized Rx antenna
25MHz – 6GHz.

## Slide 17: Data
Ground truth – detection of known transmitters:
  TV-UHF.
  Combined with FCC CDBS, AntennaWeb, TVFool and Spectrum Bridge.
Controlled – detection of custom transmitters:
  WiMax using 1.75MHz, 3.5MHz and 7MhHz bandwidth.
Artificially mixed signals.

## Slide 18: Bandwidth Detection
Detected Bandwidth, MHz

## Slide 19: Detection of Multiple Transmitters

## Slide 20: Detection of Multiple Transmitters
Multiple transmitters with variable bandwidths
Case 1
Case 2

## Slide 21: Conclusion and Future Outlook
TxMiner successfully detects key transmitter characteristics.
An integral component that enables:
  DSA beyond TV White Spaces.
  Better regulation of DSA spectrum.
  Spectrum regulation in developing countries.
Avenues for improvement:
  Channel modeling beyond log-normal (e.g. Rayleigh in fast-fading conditions).
  Detection of mobile transmitters.
  Integration with known transmitter signatures.

## Slide 22: Thank you! Questions?
Mariya Zheleva
mjeleva@gmail.com